“1 City Compost

| (i) | Moisture per cent. by weight | 15.0-25.0 |
| --- | --- | --- |
| (ii) | Colour | Dark brown to black |
| (iii) | Odour | Absence of foul odour |
| (iv) | Particle size | Minimum 90% material should pass through 4.0mm IS sieve |
| (v) | Bulk density (g/cm3) | <1.0 |
| (vi) | Total organic Carbon, per cent. by weight, minimum | 12.0 |
| (vii) | Total Nitrogen (as N) per cent. by weight, minimum | 0.8 |
| (viii) | Total Phosphates (as P2O5)per cent. by weight minimum | 0.4 |
| (ix) | Total Potash (as K2O) per cent by weight, minimum | 0.4 |
| (x) | C: N ratio | <20 |
| (xi) | pH | 6.5-7.5 |
| (xii) | Conductivity (as dsm-1) not more than | 4.0 |
| (xiii) | Pathogen | Nil |
| (xiv) | Heavy metal content (as mg/kg) Per cent. by weight maximum Arsenic (as As2O3) Cadmium (as Cd) Chromium (as Cr) Copper (as Cu) Mercury (as Hg) Nickel (as Ni) Lead (as Pb) Zinc (as Zn) | 10.00 5.00 50.00 300.00 0.15 50.00 100.00 1000.00.”; |

“2 Vermic  Compost

| (i) | Moisture per cent. by weight | 15.0-25.0 |
| --- | --- | --- |
| (ii) | Colour | Dark brown to black |
| (iii) | Odour | Absence of foul odour |
| (iv) | Particle size | Minimum 90% material should pass through 4.0mm IS sieve |
| (v) | Bulk density (g/cm3) | 0.7-0.9 |
| (vi) | Total organic Carbon, per cent. by weight, minimum | 18.0 |
| (vii) | Total Nitrogen (as N) per cent. by weight, minimum | 1.0 |
| (viii) | Total Phosphates (as P2O5)per cent. by weight minimum | 0.8 |
| (ix) | Total potassium (as K2O) per cent by weight, minimum | 0.8 |
| (x). | Heavy metal content (as mg/kg) per cent. by weight maximum Cadmium (as Cd) Chromium (as Cr) Nickel (as Ni) Lead (as Pb) | 5.00 50.00 50.00 100.00 |

“3 Phosphate Rich Organic Manure (PROM)

|  | Moisture per cent. by weight, maximum | 25.0 |
| --- | --- | --- |
|  | Particle size | Minimum 90% material should pass through 4.0mm IS sieve |
|  | Bulk density (g/cm3) | less than1.6 |
|  | Total organic Carbon, per cent. by weight, minimum | 7.9 |
|  | Total Nitrogen (as N) per cent. by weight, minimum | 0.4 |
|  | Total Phosphates (as P2O5)per cent. by weight minimum | 10.4 |
|  | C: N ratio | less than 20:1 |
|  | pH (1:5 solution) maximum | 6.7 |
|  | Conductivity (as dSm-1) not more than | 8.2 |
| . | Heavy metal content (as mg/kg) Per cent. by weight maximum Arsenic (as As2O3) Cadmium (as Cd) Chromium (as Cr) Copper (as Cu) Mercury (as Hg) Nickel (as Ni) Lead (as Pb) Zinc (as Zn) | 10.00 5.00 50.00 300.00 0.15 50.00 100.00 1000.00.”; |